## Slide 1
Neural Network based controller synthesis
Yangge Li

## Slide 2
The goal of this project is to synthesize controllers for nonlinear systems and reach-avoid requirements.
The synthesize controllers consist of a reference trajectory and tracking controller which drives the system’s state towards the reference
The tracking controller will be a neural networks controller learded from example running data
Using reachability analysis tool to calculate the error bound of the tracking controller.
Introduction

## Slide 3
The tracking controller should drive the vehicle to track a reference trajectory.
In the current setting, the tracking controller can drive the vehicle to a waypoint 15 units away from its initial position regardless of its initial orientation.
Tracking Controller

## Slide 4
In the current setting, the tracking controller can drive the vehicle to a waypoint 15 unit away from its initial position regardless of its initial orientation.
The input to the tracking controller is
  The distance between the current position of the vehicle and the reference waypoint
  The angle between the orientation of the vehicle and the line segment connecting the vehicle and reference waypoint.
  The problem is by construction translation and rotation invariant.
Tracking Controller

## Slide 5
The output to the tracking controller is the steering angle . To simplify the problem at current stage, I assume the vehicle is running at constant speed
In this work, the tracking controller is represented by a neural network. The neural network have 1 hidden layer, 100 hidden neuron. Use ReLU as activation function.
The input to the neural network is the input to the controller, which is and
The output from the neural network is the output of the controller, which is the steering angle .
Tracking Controller

## Slide 6
With the tracking controller and a vehicle model, it is able to close the loop to form a non linear autonomous system (figure 1) to be analyzed by reachability computation algorithm.
The transition graph of the system is shown in figure 2.
Use DryVR to compute the reachtube of the system. Since DryVR can handle black box model.
Computing the reachabe set

## Slide 7
The below figures shows the reach tube computed by DryVR for the vehicle with initial condition , where x, y are the position of the vehicle and is the orientation of the vehicle.
In the pictures, the reach tube for mode 1 is not plotted since the vehicle will remain stationary in that mode. The red traces in the plot shows random simulation trajectories with the neural network tracking controller.
The first plot plots time vs x. The second plot plots time vs y. The third plot plots x vs y.
Computed Reachtube

## Slide 8
With the reachtube computed, it is possible to obtain a bound for the error of tracking the reference trajectory.
The next step is to generate a reference trajectory that the vehicle can follow and can reach the goal.
Next Step